## Slide 1: Chapter 4 Engine and Refrigerators
  Heat Engine – Carnot Cycle
  Refrigerator
  Real Heat Engine

## Slide 2
Heat Engine
Steam turbines generates electricity in most of power plants
Any device that absorbs heat and converts a part of that energy into work
Examples:
Internal combustion engine used in most of today’s automobiles , does not actually absorb heat, but we can pretend that the thermal energy comes from outside rather than inside and treat it, also, as a heat engine
Th
Tc
Qh
W
Qc
Heat Source or Hot reservoir
Heat Sink or Cold reservoir
If Qh is the heat in at Th
Qc is heat dumped at Tc
The work
Ideal heat source: It gives away heat, but its temp does not change
Ideal heat sink: It absorbs heat, but its temp does not change
Efficiency

## Slide 3
To get rid of the entropy, every heat engine must dump some waste heat into heat sink (environment)
As heat flows into the engine, it brings entropy also that must be disposed off before the cycle of the engine starts over again
Heat Engine cont…
2nd Law  The total change in the entropy of engine plus surrounding
The heat reservoir is giving away heat, Qh
Its entropy , must decrease
while the cold reservoir absorbs the heat, Qc
Its entropy , must increase
Therefore,

## Slide 4
1st Law  you can not have an efficiency more than 100 %
Since energy must be conserved
2nd Law makes things even worse
 you can not even have an efficiency equals to100 %
As you can not have
or
A Carnot Cycle (engine) is an ideal heat engine with maximum efficiency
In many engine the work substance is gas
1st gas absorbs heat Qh from heat reservoir
 Entropy of heat reservoir decreases
But entropy of gas increases
will be little less than Th
Next Tgas1 remains constant by allowing gas to expand isothermally
2nd when gas dumps waste heat to cold reservoir, increases

Tgas2 will be little higher than Tc
Again, Tgas2 remains constant at this temp by isothermal compression

## Slide 5
at temperature of gas that is little less than hot reservoir temperature
Therefore, we have
Isothermal expansion
and
Isothermal Compression
at temperature of gas that is little higher than cold reservoir temperature
This will avoid creating any new entropy
The remaining part is/are
How to get gas at one temperature to another and back?
To avoid any leakage of heat during these steps, these steps must be
Adiabatic
Entire Cycle of an ideal heat engine
Isothermal expansion at
Adiabatic expansion (so that T decreases from Th to Tc)
Isothermal compression at
Adiabatic compression (so that T increases from Tc to Th)

## Slide 6: The Carnot Cycle
The gas is isothermally compressed at TC. Heat energy QC = |Q12| is removed.
The gas is adiabatically compressed, with Q = 0, until the gas temperature reaches TH.
After reaching maximum compression, the gas expands isothermally at temperature TH. Heat QH = Q34 is transferred into the gas.
The gas expands adiabatically, with Q=0, until the temperature decreases back to TC.
Work is done in all four processes of the Carnot cycle, but heat is transferred only during the two isothermal processes.

## Slide 7
Process Description
1-2 Isothermal heat addition
2-3 Isentropic expansion
3-4 Isothermal heat rejection
4-1 Isentropic compression
Carnot Cycle
Thermodynamics: An Engineering Approach, 5th edition by Yunus A. Çengel and Michael A. Boles
The Carnot cycle is the most efficient thermodynamic cycle for operating a heat engine.
It is a reversible cycle, that consists of two isotherms and two adiabats.
Adiabatic and quasistatic

## Slide 8: The Carnot Cycle

## Slide 9: Third Law of Thermodynamics
  It is impossible to reach a temperature of absolute zero.
  It is impossible to have a (Carnot) efficiency equal to 100% (this would imply Tc = 0).
The 3rd law states that as the temperature goes to zero, the entropy goes to a constant, So

## Slide 10: Example
An ideal gas is taken through the Carnot cycle. The isothermal expansion occurs at 250 oC, and the isothermal compression takes place at 50 oC. The gas takes in 1200 J of energy from the hot reservoir during the isothermal expansion. Find
  the energy expelled to the cold reservoir in each cycle and
  the net work done by the gas in each cycle.
= 250oC = 523 K
= 50oC=323 K
= 1200 J
Wout = 459 J
  QC = 741 J
  = 0.382

## Slide 11
One of the most efficient heat engines ever built is a steam turbine in the Ohio valley, operating between 430 oC and 1870 oC on energy from West Virginia coal to produce electricity for the Midwest.
  What is the maximum theoretical efficiency (the Carnot efficiency)?
  The actual efficiency of the engine is 42%. How much useful power does the engine deliver if it takes in 1.4 × 105 J of energy each second from its hot reservoir?
Example
= 430oC = 703 K
= 1870oC = 2143 K
QH = 1.4 × 105 J
= 67.2%
Wout = 58.8 kJ

## Slide 12: Problem-Solving Strategy: Heat-Engine Problems
Identify each process in the cycle
Draw the PV diagram
Visualize
Solve
There are several steps in the mathematical analysis
Use ideal-gas law to find, n, P, V and T at one point in the cycle.
Use ideal-gas law and equation for specific gas processes to determine P, V and T at the beginning and end of each process.
Calculate Q, W and ΔU.
Find Wout by adding the works in all processes. In case of simple geometry, you can confirm this y finding area enclosed within PV curve.
Add just positive values of Q to find Qh.
Verify that Δunet = 0 for a complete cycle.
Calculate the Thermal efficiency, η and any other quantity you need to complete the solution
Assess
Is Δunet = 0, Do all signs of works and heat make sense? Does η has a reasonable value? Have you answered all the questions?

## Slide 13: Refrigerators
2nd law - Heat is always transferred spontaneously from a hotter object to a colder object.
Refrigerators
  The gas in a refrigerator can extract heat QC from the cold reservoir only if the gas temperature is lower than the cold-reservoir temperature TC. Heat energy is then transferred from the cold reservoir into the colder gas.
  The gas in a refrigerator can exhaust heat QH to the hot reservoir only if the gas temperature is higher than the hot-reservoir temperature TH. Heat energy is then transferred from the warmer gas into the hot reservoir.
Tgas < TC
Tgas > TH

## Slide 14: Refrigerators
heat
work
heat
hot reservoir, TH
cold reservoir, TC
The purpose of a refrigerator is to make thermal energy flow from cold to hot. The coefficient of performance for a fridge:
entropy
COP is the largest when TH and TC are close to each other!
Note: Heat can not be transferred from low temperature to high temperature without doing extra work.

## Slide 15: More on Refrigerators
heat
work
heat
hot reservoir, TH
cold reservoir, TC
We can create a refrigerator by running a Carnot engine backwards: the gas extracts heat from the cold reservoir and deposit it in the hot reservoir.
entropy
TC
P
V
TH
1
2
3
4
rejects
heat
absorbs heat
However, it is difficult to built a practical refrigerator using such an ideal gas cycles as Carnot or Stirling. Most modern refrigerators use some liquid as a working substance. These schemes are better than a reversed Carnot cycle: much more energy can be absorbed per unit mass of working substance. Thus, the fridge can be much smaller than a Carnot fridge could be.

## Slide 16: The Maximum Efficiency
COP

## Slide 17
Assignment # 6 Due 3/25/2022
4.5, 4.6, 4.14, 4.15 & 4.23.
Problems for practice of Ch 4:
4.1, 4.2, 4.3, 4.4, 4.7, 4.8, 4.9, 4.10, 4.11, 4.18, 4.20 & 4.22.