## Slide 1: Refrigerators
heat
work
heat
hot reservoir, TH
cold reservoir, TC
The purpose of a refrigerator is to make thermal energy flow from cold to hot. The coefficient of performance for a fridge:
entropy
COP is the largest when TH and TC are close to each other!
Note: Heat can not be transferred from low temperature to high temperature without doing extra work.

## Slide 2: More on Refrigerators
heat
work
heat
hot reservoir, TH
cold reservoir, TC
We can create a refrigerator by running a Carnot engine backwards: the gas extracts heat from the cold reservoir and deposit it in the hot reservoir.
entropy
TC
P
V
TH
1
2
3
4
rejects
heat
absorbs heat
However, it is difficult to built a practical refrigerator using such an ideal gas cycles as Carnot or Stirling. Most modern refrigerators use some liquid as a working substance. These schemes are better than a reversed Carnot cycle: much more energy can be absorbed per unit mass of working substance. Thus, the fridge can be much smaller than a Carnot fridge could be.

## Slide 3: The Maximum Efficiency
COP
Real Engine
Question: How a real engine works?
We will not go in-depth of engineering but see few examples only

## Slide 4: The Stirling heat engine
Stirling engine; a simple, practical heat engine using a gas as working substance.
more practical than Carnot, and its efficiency is close to the Carnot maximum efficiency.
The Stirling engine contains a fixed amount of gas which is transferred back and forth between a "cold" and a "hot" end of a long cylinder.
The "displacer piston" moves the gas between the two ends and the "power piston" changes the internal volume as the gas expands and contracts.
T
4
1
2
3
V2
V1
T1
T2

## Slide 5
Stirling heat engine
Construction
  absorbs heat from an external source, could be anything from gasoline to solar energy to the heat produced by decaying plants.
  Working substance is air or any other gas.
  Consists of two cylinders with pistons, one in thermal contact with each reservoir.
  The pistons are connected to a crankshaft
  The gas flows past a regenerator between the two cylinders (a temporary heat sink (cold reservoir), made of wire mesh, whose temperature varies gradually from the hot side to the cold side). The heat capacity of the regenerator is very large, so its temperature is affected very little by the gas flowing past.
  The gases used inside a Stirling engine never leave the engine.
Applications: in submarines or auxiliary power generators, where quiet operation is important.
Stirling engines are very quiet = there are no exhaust valves that vent high-pressure gases, as in a gasoline or diesel engine, and there are no explosions taking place.

## Slide 6: Internal Combustion Engines (Otto cycle)
Otto cycle:
Working substance – a mixture of air and vaporized gasoline.
No hot reservoir – thermal energy is produced by burning fuel, resulting in a gas in high T and P.
Engines where the fuel is burned inside the engine cylinder as opposed to that where the fuel is burned outside the cylinder (e.g., the Stirling engine).
More economical than ideal-gas engines because a small engine can generate a considerable power.
Gasoline engine found in most automobiles

## Slide 7: Otto cycle
0  1 intake (fuel + air is pulled into the cylinder by the retreating piston)
1  2 isentropic compression
2  3 isochoric heating
3  4 isentropic expansion producing mechanical work
4  1  0 the hot exhaust gases are expelled and replaced by a new mixture at
lower T and P
P
V
1
2
3
4
ignition
exhaust
expansion
work done by gas
compression
work done on gas
V1
V2
Patm
intake/exhaust
0
The four-stroke cycle of a conventional gasoline engine.
Notes: The arrows on the piston indicate the direction of its motion during each process. (a) In the intake stroke, air and fuel enter the cylinder. (b) The intake valve is then closed, and the air–fuel mixture is compressed by the piston. (c) The mixture is ignited by the spark plug, with the result that the temperature of the mixture increases at essentially constant volume. (d) In the power stroke, the gas expands against the piston. (e) Finally, the residual gases are expelled, and the cycle repeats.

## Slide 8
S
V
1
2
3
4
V1
V2
S2
S1
- the compression ratio
The efficiency:
 = 1+2/f - the adiabatic exponent
- minimum cylinder volume
- maximum cylinder volume
Otto cycle (Cont)
Notes: PV diagram for the Otto cycle, which approximately represents the processes occurring in an internal combustion engine.

## Slide 9
As
Otto cycle (cont)
The way to improve the efficiency?
Increase compression ratio
Typically, compression ration,
 Efficiency (max) ~ 56%
While for Carnot cycle with similar temperature efficiency ~ 66%
Friction
Conductive heat loss
Incomplete combustion of the fuel
Remember
Today’s automobile engines’ efficiency ~20-30%
Factors reducing the efficiency:
But higher compression
 higher temperature increase
Gasoline can pre-ignite spontaneously before
compression is complete (before ignition stage)
Cause P to increase before point 2
(or B) on PV-diagram
This can be avoided in diesel engine
by compressing only air and then spraying fuel into the cylinder (where air is hot enough)
 Ignition starts

## Slide 10
Ideal Diesel Cycle
ignition
expansion
exhaust
compression
= V3
= V4
Diesel engine generates higher compression ration, typically ~20
Efficiency ~ 40%
Actual efficiency formula is complicated in terms of
is called cut off
Problem 4:20 Start with
Find
Remember
Only limit on efficiency is melting temperature of the material and strength to higher pressure
Ceramic engine could withstand to higher temp and pressure
 Better efficiency
Problem?
Notes: Figure 22.14 PV diagram for an ideal diesel engine.
Air undergoes adiabatic compression from A to B; at B, fuel is injected into the cylinder, mixes with the hot air and results in combustion, the fuel then undergoes constant pressure expansion from B to C; At C the fuel injection is cut off and the gas expands through an adiabatic process; the exhaust valve is opened and a constant volume output of energy occurs as the cylinder empties.

## Slide 11: Steam engine (Rankine cycle)
V
condenser
Pump
P
water
steam
Water + steam
1
2
3
4
Turbine
Adiabatic expansion
Boiler
processes
at P = const,
 Q = dH
heat
hot reservoir, TH
cold reservoir, TC
Boiler
Condenser
Turbine
Pump
W
An idealized PV-diagram of a steam engine cycle is called Rankine cycle
12 Starting at 1 (water pump) – water is pumped to
higher pressure
23 Water flows into Boiler, where it is heated at
constant pressure (It becomes steam)
34 Steam hits the turbine – expands Adiabatically
(do useful work) and cools down and ends up
original lower pressure (becomes mixture of water and steam)
41 Finally, this partially condensed fluid is cooled in
condenser (it becomes water at constant pressure)
Sadi Carnot
Notes: 1-2 water is pumped to high pressure (2) and then flows into a boiler, where (step 2-3) heat is added at constant pressure. At point 3, the steam hits the turbine, where is expands adiabatically, cools, and ends up at the original low pressure (4). The partially condensed fluid is cooled further in a condenser (a network of pipes in good thermal contact with the low-temperature reservoir.

## Slide 12
Applications: Large power plants
The steam does work by pushing a turbine,
The heat is provided by burning a fossil fuel or fissioning uranium.
Efficiency can not be calculated from PV-diagram
Rankine cycle (cont)
We must consider Enthalpy
Because of phase change involved
Efficiency,
In this case,
Since heat is absorbed and expelled at constant P, while phase changes in both stages
&

A pretty good assumptions is
Since at both stages, the phase is liquid
V
condenser
Pump
P
water
steam
Water + steam
1
2
3
4
Turbine
Adiabatic expansion
Boiler
Qh
Qc
Table 4.1 &4.2, page 136

## Slide 13: Real Refrigerators/Air Conditioners
Standard refrigeration cycle – reverse Rankine cycle
  Again the working substance changes back and forth from a gas to liquid
  But the fluid must have a much lower boiling temperature

## Slide 14
Cooling of Gases
In a refrigerated, we need to cool the gas (cooling fluid) below cold reservoir temperature
The process is called Throttling Process (also known as Joule-Thomson Process
Pi
Pf
Vi
Ti
Vf
Tf
Fluid is pushed through a piston, exerting pressure Pi in volume Vi
Second piston (moving to right) exerts backward pressure Pf in a volume Vf
This is adiabatic process – so no heat flows
0
But
Enthalpy is constant in Throttling process
For an ideal gas, this process won’t result in any T change:
H = const means T = const
for an ideal gas
Thus, we cannot cool an ideal gas by going through the Joule-Thomson process! (Similar to expansion of an ideal gas through a hole in vacuum).
Luckily, for real gases, the temperature does change in the Joule-Thomson process.

## Slide 15
For ideal gas
For dense gas or liquid
Due to forces between particles
If increases, decreases  fluid cools down
Forces between particles are weakly attractive at long distance but are strongly repulsive when particles are very close to each other and hence can be negative for under certain conditions.
in this case changes from more negative to less negative (increases)
Reading Assignment:
Liquification of gases, towards absolute zero (including laser cooling)
(P. 141 – 147)

## Slide 16: Toward Absolute Zero
10-5
109
Temperature, K
10-3
10-1
101
103
105
107
Center of hottest stars
Center of Sun,
nuclear reactions
Electronic/chemical energy
Surface of Sun, hottest boiling points
Organic life
Liquid air
Liquid 4He
Universe
Superfluid 4He
Superfluid 3He
Lowest T of condensed matter
Superconductivity
Electronic
magnetism
Nuclear
magnetism

## Slide 17
Assignment # 6 Due 3/25/2022
4.5, 4.6, 4.14, 4.15 & 4.23.
Problems for practice of Ch 4:
4.1, 4.2, 4.3, 4.4, 4.7, 4.8, 4.9, 4.10, 4.11, 4.18, 4.20 & 4.22.