## Slide 1: Steam engine (Rankine cycle)
V
condenser
Pump
P
water
steam
Water + steam
1
2
3
4
Turbine
Adiabatic expansion
Boiler
processes
at P = const,
 Q = dH
heat
hot reservoir, TH
cold reservoir, TC
Boiler
Condenser
Turbine
Pump
W
An idealized PV-diagram of a steam engine cycle is called Rankine cycle
12 Starting at 1 (water pump) – water is pumped to
higher pressure
23 Water flows into Boiler, where it is heated at
constant pressure (It becomes steam)
34 Steam hits the turbine – expands Adiabatically
(do useful work) and cools down and ends up
original lower pressure (becomes mixture of water and steam)
41 Finally, this partially condensed fluid is cooled in
condenser (it becomes water at constant pressure)
Sadi Carnot
Notes: 1-2 water is pumped to high pressure (2) and then flows into a boiler, where (step 2-3) heat is added at constant pressure. At point 3, the steam hits the turbine, where is expands adiabatically, cools, and ends up at the original low pressure (4). The partially condensed fluid is cooled further in a condenser (a network of pipes in good thermal contact with the low-temperature reservoir.

## Slide 2
Applications: Large power plants
The steam does work by pushing a turbine,
The heat is provided by burning a fossil fuel or fissioning uranium.
Efficiency can not be calculated from PV-diagram
Rankine cycle (cont)
We must consider Enthalpy
Because of phase change involved
Efficiency,
In this case,
Since heat is absorbed and expelled at constant P, while phase changes in both stages
&

A pretty good assumptions is
Since at both stages, the phase is liquid
V
condenser
Pump
P
water
steam
Water + steam
1
2
3
4
Turbine
Adiabatic expansion
Boiler
Qh
Qc
Table 4.1 &4.2, page 136

## Slide 3
Example – Efficiency of a Steam Engine
Suppose cycle operates between 0.023 bars (where boiling temperature of water is 20 oC) and the maximum pressure of 300 bars with a maximum superheated stem of 600 oC temperature. Steam after passing through turbine is converted into a mixture of a 29% water and 71% steam
At , at 20 oC
Table 4.1 
At , at 600 oC
Table 4.2 
S3 = S4 = 6.233 kJ/K
And at point 4 (on PV diagram), we have 29% steam and 71% water
Table 4.2 
Therefore
If it was a Carnot engine operating between 20 oC and 600 oC

## Slide 4: Real Refrigerators/Air Conditioners
Standard refrigeration cycle – reverse Rankine cycle
  Again the working substance changes back and forth from a gas to liquid
  But the fluid must have a much lower boiling temperature

## Slide 5
Cooling of Gases
In a refrigerated, we need to cool the gas (cooling fluid) below cold reservoir temperature
The process is called Throttling Process (also known as Joule-Thomson Process
Pi
Pf
Vi
Ti
Vf
Tf
Fluid is pushed through a piston, exerting pressure Pi in volume Vi
Second piston (moving to right) exerts backward pressure Pf in a volume Vf
This is adiabatic process – so no heat flows
0
But
Enthalpy is constant in Throttling process
For an ideal gas, this process won’t result in any T change:
H = const means T = const
for an ideal gas
Thus, we cannot cool an ideal gas by going through the Joule-Thomson process! (Similar to expansion of an ideal gas through a hole in vacuum).
Luckily, for real gases, the temperature does change in the Joule-Thomson process.

## Slide 6
For ideal gas
For dense gas or liquid
Due to forces between particles
If increases, decreases  fluid cools down
Forces between particles are weakly attractive at long distance but are strongly repulsive when particles are very close to each other and hence can be negative under certain conditions.
in this case changes from more negative to less negative (increases)
Reading Assignment:
Liquification of gases, towards absolute zero (including laser cooling)
(P. 141 – 147)

## Slide 7
Problem 4.1
Ideal atomic gas
Heat engine
(a) Efficiency? For
(b) Efficiency of an ideal engine operated between same temperatures?
Recall P 1.34, which concerned an ideal diatomic gas taken around a rectangular cycle on a PV diagram. Suppose now that this system is used as a heat engine to convert heat added into mechanical work.
P
V
P2
P1
V1
V2
A
B
C
D
PV diagram
Fig 1.10 b
Net W
Heat is absorbed during path A and B
For path A,
Ideal gas 
For path B, +W

## Slide 8
Problem 4.10
Problem 4.9
Problem 4.11
Power drawn from a wall outlet?
Qc = 300 Watts = 300 J/s
Ideal Refrigerator
50 Watts
Maximum possible COP of a refrigerator?
Assuming:
Inside Temp = 20 oC
Outside Temp = 35 oC
19.5
Maximum possible COP of a refrigerator?
Operated between 1 K and 0.01 K
~ 0.01

## Slide 9
Problem 4.20
Diesel engine (Otto cycle) efficiency
ignition
expansion
exhaust
compression
= V3
= V4
Drive formula for the efficiency of the Diesel cycle, in terms of the compression ratio
Show for a given compression ratio, the Diesel cycle is less efficient than the Otto cycle.
Evaluate the theoretical efficiency of a Diesel engine with a compression ratio of 18 and a cutoff ratio of 2.
3  4 and 1 2 are Adiabatic

## Slide 10: Toward Absolute Zero
10-5
109
Temperature, K
10-3
10-1
101
103
105
107
Center of hottest stars
Center of Sun,
nuclear reactions
Electronic/chemical energy
Surface of Sun, hottest boiling points
Organic life
Liquid air
Liquid 4He
Universe
Superfluid 4He
Superfluid 3He
Lowest T of condensed matter
Superconductivity
Electronic
magnetism
Nuclear
magnetism

## Slide 11
Assignment # 6 Due 3/25/2022
4.5, 4.6, 4.14, 4.15 & 4.23.
Problems for practice of Ch 4:
4.1, 4.2, 4.3, 4.4, 4.7, 4.8, 4.9, 4.10, 4.11, 4.18, 4.20 & 4.22.